## Slide 1
MODULE 2 · TOPIC 2
RTL Design Methodology
Basics of register transfer level (RTL) design · Overview of the RTL design process and methodology · Introduction to hardware description languages such as Verilog or VHDL
Theory 1 · What RTL is — the two kinds of logic, the synchronous discipline, four levels of abstraction
Theory 2 · The methodology — the flow, the synthesisable subset, the rules, and coding style
Theory 3 · The patterns — datapath and controller, state machines, parameters and generate
Theory 4 · HDLs — what one is, and Verilog against VHDL
Practical · Labs A–N · 26 hours · 103 exercises · every number measured
Chip Design Associate · Module 2 · Verilog RTL Coding for Synthesis · Topic 2: RTL Design Methodology
M2-T2 · 1

## Slide 2
MODULE 2 · NOS NIE/ELE/N0102
Terminal Outcomes
Chip Design Associate · Module 2 · Verilog RTL Coding for Synthesis · Topic 2: RTL Design Methodology
M2-T2 · 2
Outcome 2 names this subtopic in the NOS itself
"Level of abstraction in Verilog programming" is the phrase. This session takes one circuit down all four levels, simulates them together, and proves they are the same — which is the deliverable the outcome asks for.

## Slide 3
MODULE 2 · TOPIC 2
Key Learning Outcomes
Chip Design Associate · Module 2 · Verilog RTL Coding for Synthesis · Topic 2: RTL Design Methodology
M2-T2 · 3
Every outcome is assessed by a command you run, not by something you recite.

## Slide 4
MODULE 2 · TOPIC 2
Which Command Assesses Which Outcome
Chip Design Associate · Module 2 · Verilog RTL Coding for Synthesis · Topic 2: RTL Design Methodology
M2-T2 · 4
Run the right-hand column and you have evidence for the left-hand one.

## Slide 5
TOPIC 2 · COVERAGE
Every Syllabus Phrase, and Where It Is Covered
Chip Design Associate · Module 2 · Verilog RTL Coding for Synthesis · Topic 2: RTL Design Methodology
M2-T2 · 5
On the four notional hours
Four hours is enough to define the terms. It is not enough to make anyone believe them — and nothing in this subtopic is believed until it has been seen to happen. Lecture from the summary slides to fit four hours; run the lab alongside to teach it.

## Slide 6
TOPIC 2 · STRUCTURE
How This Session Runs
Chip Design Associate · Module 2 · Verilog RTL Coding for Synthesis · Topic 2: RTL Design Methodology
M2-T2 · 6
RTL is not a language and it is not a tool. It is a way of thinking about hardware.

## Slide 7
THEORY 1
What RTL Is
The name is the definition, and almost everything else in this topic is a consequence of it.
Registers, and what transfers into them on each clock edge
Why <= and = are not interchangeable
Four levels of abstraction, one circuit
And what a synthesiser makes of each level
Chip Design Associate · Module 2 · Verilog RTL Coding for Synthesis · Topic 2: RTL Design Methodology
M2-T2 · 7

## Slide 8
1.1 · THE DEFINITION
Register Transfer Level: the Name Is the Definition
Chip Design Associate · Module 2 · Verilog RTL Coding for Synthesis · Topic 2: RTL Design Methodology
M2-T2 · 8
Two statements, and nothing else
1. Which registers exist. 2. What transfers into each one, on each clock edge.
How many gates, which gates, how they are wired, how fast they are — none of that is in the description. You state the transfers; synthesis works out the circuit.

## Slide 9
1.1 · THE DEFINITION
Watch One Value Transfer
Chip Design Associate · Module 2 · Verilog RTL Coding for Synthesis · Topic 2: RTL Design Methodology
M2-T2 · 9
A single 5 applied on cycle 0. It reaches x, then y as 6, then z as 12, then acc — one register per clock edge, and nothing moves in between.

## Slide 10
1.2 · THE TWO KINDS
Combinational and Sequential
Chip Design Associate · Module 2 · Verilog RTL Coding for Synthesis · Topic 2: RTL Design Methodology
M2-T2 · 10
There is no third kind. Every block in this course is an arrangement of these two.

## Slide 11
1.2 · THE TWO KINDS
Side By Side
Chip Design Associate · Module 2 · Verilog RTL Coding for Synthesis · Topic 2: RTL Design Methodology
M2-T2 · 11
Each row is a rule you will use every day. Learn which column you are in before you write a line.

## Slide 12
1.2 · THE TWO KINDS
The Same Distinction, In Code
Chip Design Associate · Module 2 · Verilog RTL Coding for Synthesis · Topic 2: RTL Design Methodology
M2-T2 · 12
COMBINATIONAL
always @(*) or assign
Blocking assignment. Every output written on every path, or the tool builds a latch you did not ask for.
No clock appears anywhere in the block.
Checked by: simulation, lint.
SEQUENTIAL
always @(posedge clk)
Non-blocking assignment. Reset appears here and only here.
One value remembered per flip-flop, updated on the edge and at no other time.
Checked by: simulation, lint, and static timing analysis.
Why the two are kept in separate always blocks
A block that mixes them has to be read twice — once for what it computes and once for when. Splitting them means each block has one job, and the reviewer, the linter and the synthesiser all agree about which job it is.

## Slide 13
1.3 · THE DISCIPLINE
One Clock, One Edge, Everything
Chip Design Associate · Module 2 · Verilog RTL Coding for Synthesis · Topic 2: RTL Design Methodology
M2-T2 · 13
Almost every rule in this topic is a consequence of this one decision.

## Slide 14
1.3 · THE DISCIPLINE
What the Discipline Buys You
Chip Design Associate · Module 2 · Verilog RTL Coding for Synthesis · Topic 2: RTL Design Methodology
M2-T2 · 14
ANALYSABLE
With one clock and one edge, timing analysis is a finite question: for every path from a flip-flop to a flip-flop, does the data arrive in time? Add a gated clock and the question multiplies.
COMPOSABLE
Two blocks written to the same discipline can be wired together without a conversation. Two blocks written to different disciplines need one, every time.
REVIEWABLE
A reviewer who knows the discipline can read your block for what it computes, because the question of WHEN has already been answered the same way it always is.
TESTABLE
Scan insertion, the technique that makes a chip testable after manufacture, assumes edge-triggered flip-flops on one clock. Latches and gated clocks each need special handling.
You are allowed to break these rules. You are not allowed to break them by accident.

## Slide 15
1.4 · WHY
Why Anyone Designs At This Level
Chip Design Associate · Module 2 · Verilog RTL Coding for Synthesis · Topic 2: RTL Design Methodology
M2-T2 · 15
Behavioural / algorithmic
RTL
Gate netlist
you write
the algorithm
registers and transfers
every gate
timing
none at all
one clock period per stage
exact, per gate
synthesisable
rarely
yes — this is the target
yes, but why would you
a 10k-gate design
unbuildable
a few hundred lines
tens of thousands of lines
who writes it
architects, in C or SystemC
you
the synthesiser
RTL is the level where the trade lands correctly
High enough that a human can write and read a real design; low enough that a tool can build it without guessing at your intent.
Every industrial digital design in the last thirty years was written here. That is not fashion — it is where the abstraction pays for itself.
Above RTL you cannot say when things happen. Below it you cannot say anything else.

## Slide 16
1.5 · <= AND =
The Two Assignment Operators, and Why It Matters
Chip Design Associate · Module 2 · Verilog RTL Coding for Synthesis · Topic 2: RTL Design Methodology
M2-T2 · 16
Neither one is an error. Both are caught by the linter you build in this topic.

## Slide 17
1.5 · <= AND =
The Swap, Worked Through
Chip Design Associate · Module 2 · Verilog RTL Coding for Synthesis · Topic 2: RTL Design Methodology
M2-T2 · 17
// NON-BLOCKING - inside always @(posedge clk)
// Step 1: read every right-hand side, using the OLD values.
// Step 2: update every left-hand side, all at the same instant.
a <= b; // reads old b
b <= a; // reads old a
a and b are SWAPPED. This is what a hardware register does.
// BLOCKING - inside always @*
// Each statement finishes before the next one starts.
a = b; // a is now b
b = a; // a is already b, so this does nothing
BOTH end up holding b. This is what software does.
Why the rule is absolute rather than stylistic
Two clocked blocks using blocking assignments can see each other's half-updated values, and which one wins depends on the order the simulator happens to evaluate them in — an order the language standard deliberately does not fix.
Non-blocking assignment exists precisely to make that race impossible.

## Slide 18
1.5 · <= AND =
And What Each One Actually Builds
Chip Design Associate · Module 2 · Verilog RTL Coding for Synthesis · Topic 2: RTL Design Methodology
M2-T2 · 18
Three flip-flops against one. Nothing illegal was written, so nothing warned.

## Slide 19
1.6 · ABSTRACTION
Four Levels, One Circuit
Chip Design Associate · Module 2 · Verilog RTL Coding for Synthesis · Topic 2: RTL Design Methodology
M2-T2 · 19
The level of abstraction changes WHAT WAS WRITTEN, not what it does.

## Slide 20
1.6 · ABSTRACTION
The Same Adder, Written Four Ways
Chip Design Associate · Module 2 · Verilog RTL Coding for Synthesis · Topic 2: RTL Design Methodology
M2-T2 · 20
// BEHAVIOURAL - you describe the function
always @* {cout, sum} = a + b + cin;
// DATAFLOW - you describe the Boolean form
assign sum = a ^ b ^ cin;
assign cout = (a & b) | (b & cin) | (a & cin);
// GATE - you name every gate and every wire
xor x1 (s1, a, b); xor x2 (sum, s1, cin);
and a1 (ab, a, b); and a2 (bc, b, cin); and a3 (ac, a, cin);
or o1 (cout, ab, bc, ac);
// SWITCH - you place individual transistors
pmos p1 (y, vdd, a); nmos n1 (y, gnd, a); // one CMOS inverter

## Slide 21
1.6 · ABSTRACTION
And What a Synthesiser Makes of Each
Chip Design Associate · Module 2 · Verilog RTL Coding for Synthesis · Topic 2: RTL Design Methodology
M2-T2 · 21
The behavioural description produced the SMALLEST circuit — and dataflow and gate produced the identical netlist.

## Slide 22
1.6 · ABSTRACTION
The Rule This Gives You
Chip Design Associate · Module 2 · Verilog RTL Coding for Synthesis · Topic 2: RTL Design Methodology
M2-T2 · 22
Write at the highest level that expresses your intent
Every level you descend takes a decision away from the tool and gives it to you — whether or not you wanted it.
What the tool is better at than you
Choosing a gate mix for a Boolean function.
Balancing a logic tree.
Meeting a timing constraint by restructuring.
Doing all of that again, consistently, at 3 a.m.
What you are better at than the tool
How many clock cycles the job should take.
Where the registers go.
What is shared and what is duplicated.
What the interface should look like.
Give the tool the first list. Keep the second one for yourself.

## Slide 23
1.7 · PROOF
Simulation Shows. Proof Settles.
Chip Design Associate · Module 2 · Verilog RTL Coding for Synthesis · Topic 2: RTL Design Methodology
M2-T2 · 23
A checker that cannot fail is not evidence of anything — which is why the lab includes a deliberately broken adder.

## Slide 24
1.8 · THE RUNNING EXAMPLE
One Design, Carried All the Way Through
Chip Design Associate · Module 2 · Verilog RTL Coding for Synthesis · Topic 2: RTL Design Methodology
M2-T2 · 24
Four bits, an asynchronous reset, an enable and a terminal count. Small enough to read in one glance, big enough to be a real design.

## Slide 25
1.8 · THE RUNNING EXAMPLE
Read It Line By Line
Chip Design Associate · Module 2 · Verilog RTL Coding for Synthesis · Topic 2: RTL Design Methodology
M2-T2 · 25
module counter4 (
input clk,
input rst_n, // asynchronous, active LOW
input en,
output reg [3:0] count,
output tc // one cycle high at 15
);
always @(posedge clk or negedge rst_n) begin
if (!rst_n) count <= 4'd0; // reset wins
else if (en) count <= count + 4'd1;
end // no else: HOLD
assign tc = en & (count == 4'd15);
endmodule
Four decisions are visible in fourteen lines
The reset is ASYNCHRONOUS, so it is in the sensitivity list; it is ACTIVE LOW, so the port is named rst_n and the test is !rst_n. Reset is tested FIRST, so it wins over the enable. And the missing else is deliberate — in a CLOCKED block, no assignment means hold, which is what a flip-flop does anyway.

## Slide 26
1.8 · THE RUNNING EXAMPLE
The Numbers, Worked Out
Chip Design Associate · Module 2 · Verilog RTL Coding for Synthesis · Topic 2: RTL Design Methodology
M2-T2 · 26
Derive the formula, then measure it. A testbench that only ever tries one value of N has told you almost nothing.

## Slide 27
THEORY 1 · CHECKPOINT
Nine Questions
Chip Design Associate · Module 2 · Verilog RTL Coding for Synthesis · Topic 2: RTL Design Methodology
M2-T2 · 27
#
Question
The answer in one line
1
What two things does an RTL description state?
which registers exist, and what transfers into them
2
What does <= mean inside a clocked block?
read all right-hand sides first, then update together
3
Name the four levels of abstraction.
behavioural, dataflow, gate, switch
4
Which level produced the smallest netlist, and why?
behavioural — it left the tool free to choose
5
Why did dataflow and gate give identical netlists?
writing the Boolean form already fixes the structure
6
Why prove equivalence instead of simulating?
exhaustive simulation stops being possible at ~30 inputs
7
What are the only two kinds of digital logic?
combinational and sequential — there is no third
8
Name three things the synchronous discipline buys you.
analysable timing, composable blocks, testable silicon
9
In counter4, why is there no else on the enable?
in a clocked block, no assignment means hold
Theory 2 asks what you are allowed to write, and why the rules exist.

## Slide 28
THEORY 2
The RTL Design Process and Methodology
Methodology is the hardest thing to teach, because the honest version is a list of habits and the dishonest version is a list of slogans.
The design flow, and where this topic sits in it
The synthesisable subset — measured, not asserted
The bug that makes simulation and silicon disagree
Seven coding rules, and a tool that checks them
Micro-architecture: the decisions RTL cannot make for you
Chip Design Associate · Module 2 · Verilog RTL Coding for Synthesis · Topic 2: RTL Design Methodology
M2-T2 · 28

## Slide 29
2.1 · THE FLOW
The RTL Design Flow
Chip Design Associate · Module 2 · Verilog RTL Coding for Synthesis · Topic 2: RTL Design Methodology
M2-T2 · 29
Every arrow points both ways in practice: a timing failure sends you back to the RTL, a synthesis surprise back to the micro-architecture.

## Slide 30
2.1 · THE FLOW
Executed, Not Described
Chip Design Associate · Module 2 · Verilog RTL Coding for Synthesis · Topic 2: RTL Design Methodology
M2-T2 · 30
make flow stops at the first stage that fails. That is what makes it a methodology rather than a diagram.

## Slide 31
2.2 · THE SUBSET
Which Verilog Actually Synthesises
Chip Design Associate · Module 2 · Verilog RTL Coding for Synthesis · Topic 2: RTL Design Methodology
M2-T2 · 31
Eleven constructs, run through a real synthesiser. The table is measured, not remembered.

## Slide 32
2.2 · THE SUBSET
Three Rows Worth Discussing
Chip Design Associate · Module 2 · Verilog RTL Coding for Synthesis · Topic 2: RTL Design Methodology
M2-T2 · 32
371 cells against 0
a / b where b is a signal builds a full combinational divider — 371 cells.
a / 4 builds nothing at all. It is a rename of wires.
Same operator. The difference is entirely what you divided BY.
#5 vanished silently
A delay is a simulation instruction. Silicon has no way to wait five time units.
Synthesis ignored it and built the gate. Your simulation and your chip now behave differently.
initial was accepted
Yosys targets FPGAs, where the bitstream really does initialise the flops.
An ASIC flow would not. This is how code that works on an FPGA fails on an ASIC.
The habit this table is for
Before you write a construct you are unsure about, synthesise a ten-line module containing only that construct and read what came out. It takes two minutes and it is the only way to actually know.

## Slide 33
2.3 · THE LATCH
The Most Common RTL Bug There Is
Chip Design Associate · Module 2 · Verilog RTL Coding for Synthesis · Topic 2: RTL Design Methodology
M2-T2 · 33
It is not an error. The tool builds it, mentions it in a log nobody reads, and hands you the design.

## Slide 34
2.3 · THE LATCH
Why a Latch In the Middle of Your Logic Hurts
Chip Design Associate · Module 2 · Verilog RTL Coding for Synthesis · Topic 2: RTL Design Methodology
M2-T2 · 34
A flip-flop
A latch
captures
on the clock EDGE
while the enable is HIGH
is transparent
never
for the whole enable window
timing analysis
one clean check per edge
time-borrowing; much harder to analyse
in a scan chain
standard
usually needs special handling
you asked for it
yes, by writing posedge
no — you forgot an else
So the rule is mechanical
In a combinational block, assign every output on every path. An if needs an else; a case needs a default. If you would rather not write them out, assign a default value at the top of the block and let later assignments override it.
Rules L005 and L006 of the linter catch this, and make lintcheck confirms the linter agrees with Yosys on every file.

## Slide 35
2.4 · THE WORST BUG
When Simulation and Silicon Disagree
Chip Design Associate · Module 2 · Verilog RTL Coding for Synthesis · Topic 2: RTL Design Methodology
M2-T2 · 35
One disagreement in six — and nothing anywhere reported an error.

## Slide 36
2.4 · THE WORST BUG
Why This Class of Bug Is Special
Chip Design Associate · Module 2 · Verilog RTL Coding for Synthesis · Topic 2: RTL Design Methodology
M2-T2 · 36
Most bugs are found by testing. This one cannot be, because the thing you are testing is not the thing that will be built. Every test you write passes, and the chip still fails.
Cause
What simulation does
What synthesis does
incomplete sensitivity list
the block sleeps; the output goes stale
ignores the list; builds the logic
# delays in RTL
waits the specified time
ignores them entirely
initial block (ASIC)
sets the value at time zero
ignores it; the flop powers up unknown
blocking in a clocked block
result depends on evaluation order
builds one specific circuit
All four have the same cure
Use always @* and never a hand-written sensitivity list. No delays in RTL. A real reset instead of an initial block. Non-blocking in clocked blocks. Then lint for all four, so that nobody has to remember.

## Slide 37
2.5 · THE RULES
Seven Rules, Checked By a Tool
Chip Design Associate · Module 2 · Verilog RTL Coding for Synthesis · Topic 2: RTL Design Methodology
M2-T2 · 37
A linter that cries wolf gets switched off. One that stays quiet is worse than none at all.

## Slide 38
2.5 · THE RULES
The Coding Standard, In One Place
Chip Design Associate · Module 2 · Verilog RTL Coding for Synthesis · Topic 2: RTL Design Methodology
M2-T2 · 38
None of these are style preferences. Every one exists because breaking it produces a design that simulates differently from the way it is built.

## Slide 39
2.6 · MICRO-ARCHITECTURE
The Decisions RTL Cannot Make For You
Chip Design Associate · Module 2 · Verilog RTL Coding for Synthesis · Topic 2: RTL Design Methodology
M2-T2 · 39
Make these on paper, before the first line of RTL. A synthesiser will faithfully build whatever you chose.

## Slide 40
2.7 · REUSE
Writing RTL That Someone Else Can Use
Chip Design Associate · Module 2 · Verilog RTL Coding for Synthesis · Topic 2: RTL Design Methodology
M2-T2 · 40
Module 2's fourth terminal outcome asks for this by name
"Emulate, debug and characterise reusable IPs." Reuse is not something you add to a design afterwards — it is a set of decisions you take while writing it, and every one of them is listed above.

## Slide 41
2.8 · STYLE
One Function, Three Coding Styles
Chip Design Associate · Module 2 · Verilog RTL Coding for Synthesis · Topic 2: RTL Design Methodology
M2-T2 · 41
Proved equivalent by SAT — and still three different netlists.

## Slide 42
2.8 · STYLE
What To Take From That
Chip Design Associate · Module 2 · Verilog RTL Coding for Synthesis · Topic 2: RTL Design Methodology
M2-T2 · 42
EQUIVALENT is not IDENTICAL
A formal equivalence proof answers exactly one question: do these two descriptions compute the same function?
It says nothing about area, nothing about timing and nothing about power. Those are separate questions with separate tools.
MEASURE YOUR OWN TOOL
The claim 'the optimiser flattens the difference' is the most repeated statement in RTL teaching, and on this toolchain it is false: 3, 6 and 10 cells.
A different synthesiser may well close the gap. Find out rather than assume.
SO WHICH DO YOU WRITE?
Whichever reads best to the next person, which is usually the case statement for anything with more than three branches.
Then measure, and only reach for the terse form if the block is actually on a critical path.
Why the three differ at all
The conditional expression hands sel[1] and sel[0] straight to the multiplexer selects. The case and if/else versions ask the tool to build equality comparators against 2'b00, 2'b01 and so on, and then to work out for itself that those comparisons ARE the select bits. It gets part of the way.

## Slide 43
THEORY 2 · CHECKPOINT
Nine Questions
Chip Design Associate · Module 2 · Verilog RTL Coding for Synthesis · Topic 2: RTL Design Methodology
M2-T2 · 43
#
Question
The answer in one line
1
Name the first four stages of the flow.
spec, micro-architecture, RTL coding, lint
2
Why lint before simulating?
it costs seconds and catches what tests cannot
3
What builds a latch?
a combinational block that does not assign on every path
4
a / b against a / 4 — what did they cost?
371 cells against 0
5
Why is an incomplete sensitivity list so dangerous?
simulation and synthesis then build different circuits
6
What does # do in synthesisable RTL?
nothing at all — it is silently ignored
7
Name three decisions synthesis will not make for you.
cycle count, register placement, sharing, interface
8
Does formal equivalence say anything about area?
no — equivalent is not the same as identical
9
The three mux styles: how many cells each?
3, 6 and 10 — style did reach the netlist here
Theory 3 is about the patterns every real block is built from.

## Slide 44
THEORY 3
The Patterns Every Block Is Built From
Three structures account for almost all synthesisable RTL. Once you can recognise them, most designs stop looking unfamiliar.
Datapath and controller — the split that organises everything else
The finite state machine, and the three-block way to write one
Moore against Mealy, in structure and in measured timing
State encoding, and what it actually costs
Parameters, hierarchy and generate: from a module to an IP
Chip Design Associate · Module 2 · Verilog RTL Coding for Synthesis · Topic 2: RTL Design Methodology
M2-T2 · 44

## Slide 45
3.1 · THE SPLIT
Datapath and Controller
Chip Design Associate · Module 2 · Verilog RTL Coding for Synthesis · Topic 2: RTL Design Methodology
M2-T2 · 45
A UART, a cache, a GPU. Different sizes, the same two halves.

## Slide 46
3.1 · THE SPLIT
The Worked Example: Accumulate N Samples
Chip Design Associate · Module 2 · Verilog RTL Coding for Synthesis · Topic 2: RTL Design Methodology
M2-T2 · 46
// the CONTROLLER decides. Narrow. No data passes through it.
always @(*) begin
acc_clr = 0; acc_en = 0; cnt_ld = 0; cnt_dec = 0; done = 0;
case (state)
S_IDLE : if (start) begin acc_clr=1; cnt_ld =1; end
S_RUN : if (!cnt_done) begin acc_en =1; cnt_dec=1; end
S_DONE : done =1;
endcase
end
// the DATAPATH holds and transforms. Wide. It decides nothing.
always @(posedge clk or negedge rst_n)
if (!rst_n) sum <= 0;
else if (acc_clr) sum <= 0;
else if (acc_en) sum <= sum + data;
Read the interface between them
Four control wires down, one status wire up. That is the entire contract. The controller never touches sum; the datapath never looks at state.

## Slide 47
3.1 · THE SPLIT
Measured, On the Accumulator
Chip Design Associate · Module 2 · Verilog RTL Coding for Synthesis · Topic 2: RTL Design Methodology
M2-T2 · 47
module
cells
flip-flops
what it contains
accum_ctrl
10
2
three states, five control outputs
accum_datapath
145
24
a 16-bit accumulator, an 8-bit down-counter
accum_top
156
26
both, plus the wires between them
Six per cent of the cells, one hundred per cent of the behaviour
That ratio is the whole argument for the split. You will re-time, widen and pipeline the expensive half many times over the life of a design — and each time, the half that decides what happens stays exactly as it was.
It also means the part that is hardest to get right is the part small enough to read in one sitting.
make dpctrl prints every control signal on every cycle, next to the accumulated sum.

## Slide 48
3.2 · THE FSM
The Three-Block Coding Pattern
Chip Design Associate · Module 2 · Verilog RTL Coding for Synthesis · Topic 2: RTL Design Methodology
M2-T2 · 48
Every state machine in this lab is written exactly like this. So is most industrial RTL.

## Slide 49
3.2 · THE FSM
Why Not One Block?
Chip Design Associate · Module 2 · Verilog RTL Coding for Synthesis · Topic 2: RTL Design Methodology
M2-T2 · 49
You can write a working state machine in a single clocked block, with the case statement inside it. Nothing about it is illegal.
one block
three blocks
works?
yes
yes
where is the reset?
mixed in with the logic
block 1, and nowhere else
where is the clock?
wrapped around everything
block 1, and nowhere else
outputs are
registered, always
your choice — Moore or Mealy
reviewing a change
you re-read the timing every time
blocks 2 and 3 have no timing to re-read
adding a state
one place, easy to miss a branch
two places, both of them a case statement
One block is not wrong. Three blocks are easier to be right in, which over a project is the same thing.

## Slide 50
3.2 · THE FSM
The Default Assignment, and Why It Matters
Chip Design Associate · Module 2 · Verilog RTL Coding for Synthesis · Topic 2: RTL Design Methodology
M2-T2 · 50
always @(*) begin
next_state = state; // <-- THE DEFAULT ASSIGNMENT
case (state)
S_MAIN_GREEN : if (car && timeout) next_state = S_MAIN_YELLOW;
S_MAIN_YELLOW : if (timeout) next_state = S_SIDE_GREEN;
...
endcase
end
// Not one of those if statements has an else. Not one of them needs
// one: next_state was already written, unconditionally, on line 2.
// No path through this block leaves it unassigned, so no latch.
This is the idiom the lab linter had to learn
A naive latch rule flags every one of those if statements. Yosys builds a latch in none of them. make lintcheck puts the two opinions side by side on sixteen designs — and a linter that cries wolf gets switched off, which makes it worse than no linter at all.

## Slide 51
3.3 · MOORE AND MEALY
Where the Output Comes From
Chip Design Associate · Module 2 · Verilog RTL Coding for Synthesis · Topic 2: RTL Design Methodology
M2-T2 · 51
One structural difference — whether the output logic can see the input. Everything else follows.

## Slide 52
3.3 · MOORE AND MEALY
The Differences, In One Table
Chip Design Associate · Module 2 · Verilog RTL Coding for Synthesis · Topic 2: RTL Design Methodology
M2-T2 · 52
Five rows. The last one is measured, not assumed.

## Slide 53
3.3 · MOORE AND MEALY
The '101' Detector, Moore
Chip Design Associate · Module 2 · Verilog RTL Coding for Synthesis · Topic 2: RTL Design Methodology
M2-T2 · 53
Four states. The output is decoded from the state register alone.

## Slide 54
3.3 · MOORE AND MEALY
The Same Detector, Mealy
Chip Design Associate · Module 2 · Verilog RTL Coding for Synthesis · Topic 2: RTL Design Methodology
M2-T2 · 54
Three states. The output is written on the arrows, as input / output.

## Slide 55
3.3 · MOORE AND MEALY
The One-Cycle Difference, Measured
Chip Design Associate · Module 2 · Verilog RTL Coding for Synthesis · Topic 2: RTL Design Methodology
M2-T2 · 55
Five matches, zero mismatches against a golden model computed from the stream itself.

## Slide 56
3.3 · MOORE AND MEALY
Choosing Between Them
Chip Design Associate · Module 2 · Verilog RTL Coding for Synthesis · Topic 2: RTL Design Methodology
M2-T2 · 56
CHOOSE MOORE
when the output leaves the block, drives other logic, or is timing critical. It comes out of a decode of registered bits, so it is clean, predictable and easy to constrain.
CHOOSE MEALY
when the cycle genuinely matters — a handshake that must be answered immediately, or a pipeline where one more cycle of latency costs throughput you cannot spare.
EITHER WAY, REGISTER IT AT THE BOUNDARY
A Mealy output that leaves your block hands the next designer a combinational path they did not ask for. If it crosses a module boundary, put a flip-flop on it — which turns it back into Moore.
The trap in the folklore
"Mealy needs fewer states" is true and almost never the reason to pick it. Here it saved one flip-flop's worth of nothing — both machines needed two — and cost one cell more. The real trade is the cycle against the glitch-free output, and that is a system question, not a coding one.

## Slide 57
3.4 · ENCODING
The Choice You Make By Typing Numbers
Chip Design Associate · Module 2 · Verilog RTL Coding for Synthesis · Topic 2: RTL Design Methodology
M2-T2 · 57
Same behaviour, different hardware — and the direction of the difference is not the one usually quoted.

## Slide 58
3.4 · ENCODING
Which Encoding, and When
Chip Design Associate · Module 2 · Verilog RTL Coding for Synthesis · Topic 2: RTL Design Methodology
M2-T2 · 58
Three encodings, three different reasons. None of them is a default.

## Slide 59
3.5 · A CONTROLLER WITH A TIMER
The Traffic Light
Chip Design Associate · Module 2 · Verilog RTL Coding for Synthesis · Topic 2: RTL Design Methodology
M2-T2 · 59
Two safety properties, checked on every one of forty cycles. Zero violations.

## Slide 60
3.5 · A CONTROLLER WITH A TIMER
Checking a Property Instead of a Waveform
Chip Design Associate · Module 2 · Verilog RTL Coding for Synthesis · Topic 2: RTL Design Methodology
M2-T2 · 60
// P1 : the two roads are never green at the same time
if (main_light == GREEN && side_light == GREEN) begin
$display("*** P1 VIOLATED at cycle %0d", cycles);
errors = errors + 1;
end
// P2 : a green never goes straight to red - yellow comes first
if (prev_main == GREEN && main_light == RED) begin
$display("*** P2 VIOLATED at cycle %0d", cycles);
errors = errors + 1;
end
You write the rule once; the simulator tests it every cycle of every run
This is the cheap half of formal verification, available in any simulator, in about ten lines. It scales to runs far longer than anyone would page through by hand, and it keeps working after you change the design.
The expensive half — proving the property holds for every possible input — is what make prove does with a SAT solver.

## Slide 61
3.6 · FROM MODULE TO IP
Parameters, Hierarchy and Generate
Chip Design Associate · Module 2 · Verilog RTL Coding for Synthesis · Topic 2: RTL Design Methodology
M2-T2 · 61
Eight flip-flops per stage, exactly N stages, measured at four depths.

## Slide 62
3.6 · FROM MODULE TO IP
What Elaboration Actually Does
Chip Design Associate · Module 2 · Verilog RTL Coding for Synthesis · Topic 2: RTL Design Methodology
M2-T2 · 62
module delayline #(parameter W = 8, parameter N = 4)
(input clk, rst, en, input [W-1:0] din,
output [W-1:0] dout);
wire [W-1:0] tap [0:N]; // one more element than stages
assign tap[0] = din;
genvar k;
generate
for (k = 0; k < N; k = k + 1) begin : stage
preg #(.W(W)) u_reg (.clk(clk), .rst(rst), .en(en),
.d(tap[k]), .q(tap[k+1]));
end
endgenerate
assign dout = tap[N];
endmodule
The for loop is an instruction to the ELABORATOR, not a loop in hardware. After elaboration there are N preg instances and no loop anywhere.

## Slide 63
THEORY 3 · CHECKPOINT
Eight Questions
Chip Design Associate · Module 2 · Verilog RTL Coding for Synthesis · Topic 2: RTL Design Methodology
M2-T2 · 63
#
Question
The answer in one line
1
What are the two halves of almost every block?
a datapath that holds, a controller that decides
2
What crosses between them?
control signals down, status signals up
3
Name the three blocks of an FSM.
state register, next-state logic, output logic
4
Why does a default assignment prevent a latch?
every output is written before any branch runs
5
What does the output logic read in a Moore machine?
the state, and nothing else
6
How much later does a Moore output appear?
exactly one clock cycle, every time
7
One-hot: fewer or more flip-flops than binary?
more — one per state instead of log2(states)
8
Does a generate loop exist in the netlist?
no — it is elaborated away before synthesis
Theory 4 is about the notation — which turns out to be the least important part.

## Slide 64
THEORY 4
Introduction to Hardware Description Languages
The syllabus says "HDLs such as Verilog or VHDL". The word doing the work is OR.
Why an HDL is not a programming language
Everything happens at once
The parts of a module, and the word reg that confuses everyone
Verilog and VHDL as reference cards, and a line-for-line mapping
The anatomy of a testbench that checks itself
Both languages actually run, and their transcripts diffed
Chip Design Associate · Module 2 · Verilog RTL Coding for Synthesis · Topic 2: RTL Design Methodology
M2-T2 · 64

## Slide 65
4.1 · NOT A PROGRAM
An HDL Is Not a Programming Language
Chip Design Associate · Module 2 · Verilog RTL Coding for Synthesis · Topic 2: RTL Design Methodology
M2-T2 · 65
You are not writing instructions for a machine to follow. You are writing a description of a machine.

## Slide 66
4.2 · CONCURRENCY
Everything Happens At Once
Chip Design Associate · Module 2 · Verilog RTL Coding for Synthesis · Topic 2: RTL Design Methodology
M2-T2 · 66
Write those three assign lines in any order you like — the circuit is identical.

## Slide 67
4.3 · ANATOMY
The Parts of a Verilog Module
Chip Design Associate · Module 2 · Verilog RTL Coding for Synthesis · Topic 2: RTL Design Methodology
M2-T2 · 67
reg does not mean register. What creates a flip-flop is assigning inside always @(posedge clk) — nothing else.

## Slide 68
4.4 · SIMULATION
How a Simulator Runs an HDL
Chip Design Associate · Module 2 · Verilog RTL Coding for Synthesis · Topic 2: RTL Design Methodology
M2-T2 · 68
The order blocks are evaluated in is genuinely unspecified. That is why non-blocking assignment exists.

## Slide 69
4.5 · REFERENCE
Verilog On One Page
Chip Design Associate · Module 2 · Verilog RTL Coding for Synthesis · Topic 2: RTL Design Methodology
M2-T2 · 69
Not the whole language — the part that synthesises, which is much smaller.

## Slide 70
4.5 · REFERENCE
Verilog: Blocks and Operators
Chip Design Associate · Module 2 · Verilog RTL Coding for Synthesis · Topic 2: RTL Design Methodology
M2-T2 · 70
Three kinds of block, and the operators you will actually use.

## Slide 71
4.5 · REFERENCE
VHDL On One Page
Chip Design Associate · Module 2 · Verilog RTL Coding for Synthesis · Topic 2: RTL Design Methodology
M2-T2 · 71
Everything on this page has an exact counterpart on the previous one.

## Slide 72
4.5 · REFERENCE
VHDL: Types, and What They Catch
Chip Design Associate · Module 2 · Verilog RTL Coding for Synthesis · Topic 2: RTL Design Methodology
M2-T2 · 72
The type system is the real difference between the two languages.

## Slide 73
4.5 · REFERENCE
Verilog to VHDL, Line For Line (1 of 2)
Chip Design Associate · Module 2 · Verilog RTL Coding for Synthesis · Topic 2: RTL Design Methodology
M2-T2 · 73
Learn one and you can read the other in an afternoon. These two tables are the afternoon.

## Slide 74
4.5 · REFERENCE
Verilog to VHDL, Line For Line (2 of 2)
Chip Design Associate · Module 2 · Verilog RTL Coding for Synthesis · Topic 2: RTL Design Methodology
M2-T2 · 74
Nothing in this topic depends on which one you use.

## Slide 75
4.5 · REFERENCE
What a Testbench Is Made Of
Chip Design Associate · Module 2 · Verilog RTL Coding for Synthesis · Topic 2: RTL Design Methodology
M2-T2 · 75
Topic 5 covers verification properly. These six parts are the minimum you need to finish Topic 2.

## Slide 76
4.6 · TWO LANGUAGES
Verilog and VHDL, Side By Side
Chip Design Associate · Module 2 · Verilog RTL Coding for Synthesis · Topic 2: RTL Design Methodology
M2-T2 · 76
None of those differences are about hardware. Both describe registers, logic and hierarchy; both synthesise to the same gates.

## Slide 77
4.6 · TWO LANGUAGES
Both Designs, In Both Languages, Actually Run
Chip Design Associate · Module 2 · Verilog RTL Coding for Synthesis · Topic 2: RTL Design Methodology
M2-T2 · 77
Not "they look similar"
Both transcripts were compared line by line by diff, and there was nothing to report. The state machine is the interesting one: VHDL gives the states a real enumerated TYPE, so an illegal state will not compile. Verilog gives them numbers.

## Slide 78
4.7 · WHICH ONE
Which HDL Should You Learn?
Chip Design Associate · Module 2 · Verilog RTL Coding for Synthesis · Topic 2: RTL Design Methodology
M2-T2 · 78
Learn the concepts. The notation follows in an afternoon.

## Slide 79
THEORY 4 · CHECKPOINT
Seven Questions
Chip Design Associate · Module 2 · Verilog RTL Coding for Synthesis · Topic 2: RTL Design Methodology
M2-T2 · 79
#
Question
The answer in one line
1
Name the biggest difference between an HDL and a program.
everything in an HDL runs all the time, concurrently
2
Does the order of assign statements matter?
no — they describe hardware that exists together
3
What does reg actually mean?
assigned in a procedural block; NOT a flip-flop
4
Why is the evaluation order unspecified?
the standard leaves it free; <= makes it not matter
5
Verilog or VHDL?
either — the concepts are identical, and the lab proves it
6
What does VHDL catch that Verilog does not?
illegal states, non-exhaustive cases, width mismatches
7
Where must a testbench's expected answer come from?
the stimulus — never from the design under test

## Slide 80
PRACTICAL
Labs A–N
26 hours, 103 graded exercises, and not one number in this deck that you cannot reproduce yourself.
Which tool answers which question, and how to install them
Labs A–D: what RTL means, the ladder, proof, and the subset
Labs E–H: the mismatch, the coding rules, style, and the two pitfalls
Labs I–L: state machines, a controller with a timer, datapath and controller, and reuse
Labs M–N: two languages, the whole flow, and the vendor tools
Chip Design Associate · Module 2 · Verilog RTL Coding for Synthesis · Topic 2: RTL Design Methodology
M2-T2 · 80

## Slide 81
PRACTICAL · TOOLS
The Tools, and What Each One Is For
Chip Design Associate · Module 2 · Verilog RTL Coding for Synthesis · Topic 2: RTL Design Methodology
M2-T2 · 81
Yosys is the interesting one: the only free tool here that both synthesises your RTL and PROVES the netlist matches it.

## Slide 82
PRACTICAL · INSTALL
Two apt Lines, and the Whole Lab Runs
Chip Design Associate · Module 2 · Verilog RTL Coding for Synthesis · Topic 2: RTL Design Methodology
M2-T2 · 82
No licence, no account, no download manager. Two lines and the whole lab runs.

## Slide 83
PRACTICAL · INSTALL
The Vendor Tools the Syllabus Names
Chip Design Associate · Module 2 · Verilog RTL Coding for Synthesis · Topic 2: RTL Design Methodology
M2-T2 · 83
They add a real device library and a flow you will meet at work. They add nothing to the concepts.

## Slide 84
PRACTICAL · THE FLOW
Four Questions About One Piece of Code
Chip Design Associate · Module 2 · Verilog RTL Coding for Synthesis · Topic 2: RTL Design Methodology
M2-T2 · 84
Does it follow the rules? Does it do what the spec says? What will be built? Is that still your design?

## Slide 85
PRACTICAL · MAP
Fourteen Parts, Twenty-Six Hours
Chip Design Associate · Module 2 · Verilog RTL Coding for Synthesis · Topic 2: RTL Design Methodology
M2-T2 · 85
A–D build the mental model, E–H the methodology, I–L the patterns every block is built from, M–N the connection to other languages and real tools.

## Slide 86
LABS A–C
What RTL Means, the Ladder, and Proof
Chip Design Associate · Module 2 · Verilog RTL Coding for Synthesis · Topic 2: RTL Design Methodology
M2-T2 · 86
A · what RTL means (1 h)
Run make transfer. Follow a single 5 through four registers.
Predict the value in each register on each cycle BEFORE running it.
Deliverable: the table, and why y is 1 on cycle 0.
B · the ladder (2 h)
Write the same full adder at all four levels.
Run make ladder — all four together, exhaustively.
Then synthesise each and compare cell counts.
Deliverable: why behavioural won.
C · proof (2 h)
Run make prove. Three pairs proved equivalent.
Then break the adder yourself and watch the checker catch it.
Deliverable: why 8 patterns was enough here and will not be next time.
The exercise that teaches the most is C
Delete a different term from fa_broken.v and predict which input pattern the solver will find. Getting that prediction right means you understand both the circuit and the tool.

## Slide 87
LABS D–F
The Subset, the Mismatch, and the Rules
Chip Design Associate · Module 2 · Verilog RTL Coding for Synthesis · Topic 2: RTL Design Methodology
M2-T2 · 87
$ make subset
s03_latch OK 1 YES inferred a LATCH: $_DLATCH_P_
s08_whileloop REFUSED - - "only allowed in constant functions"
s10_divide OK 371 no a full combinational divider
s11_shift OK 0 no no logic at all - just wires
$ make mismatch
change b (list ASLEEP) a=1 b=1 RTL y=0 NETLIST y=1 <-- THEY DISAGREE
$ make lintcheck
10 files · linter and Yosys agree on every one · 0 disagreements
Exercise
Task
D.1
Predict the cell count for each construct before running make subset
D.2
Add a twelfth construct of your own and predict the result
E.1
Explain the mismatch to someone who has not seen it, in three sentences
F.1
Add rule L008 to the linter — your choice — and justify it
F.2
Find a file the linter gets wrong, and say why regexes cannot fix it

## Slide 88
LABS G–H
Coding Style, and the Two Pitfalls
Chip Design Associate · Module 2 · Verilog RTL Coding for Synthesis · Topic 2: RTL Design Methodology
M2-T2 · 88
$ make mux
mux4_assign vs mux4_case EQUIVALENT (proved, 92 SAT variables)
mux4_assign 3 cells 0 flip-flops
mux4_if 6 cells 0 flip-flops
mux4_case 10 cells 0 flip-flops
$ make pitfalls
non-blocking version : 0 wrong cycles
blocking version : 6 wrong cycles
shift_nb (non-blocking) 3 cells 3 flip-flops
shift_bl (blocking) 1 cells 1 flip-flops
s03_latch (missing else) 1 cells *** 1 LATCH INFERRED ***
Exercise
Task
G.1
Predict the three cell counts before you run make mux
G.2
Write a fourth style of your own and predict where it lands
H.1
Predict q_bl for the first six cycles, then run it
H.2
Explain in two sentences why no tool warned about shift_bl
H.3
Add an else to s03_latch and confirm the latch disappears

## Slide 89
LABS I–K
State Machines, a Timer, and a Datapath
Chip Design Associate · Module 2 · Verilog RTL Coding for Synthesis · Topic 2: RTL Design Methodology
M2-T2 · 89
$ make fsm
matches in the stream : 5 mismatches vs golden : 0
PASS - same language, Moore trails Mealy by one cycle,
and the one-hot encoding is indistinguishable
seq101_moore binary 13 cells 2 flip-flops
seq101_moore one-hot 30 cells 4 flip-flops
cycles checked : 40 property violations : 0 (traffic light)
$ make dpctrl
golden total : 157 hardware sum : 157
accum_ctrl (controller) 10 cells 2 flip-flops
accum_datapath (datapath) 145 cells 24 flip-flops
Exercise
Task
I.1
Draw the state diagram for '110' before you write any code
I.2
Write it in both styles and confirm the one-cycle offset
I.3
Re-encode the Moore machine as gray and measure the cells
J.1
Add a pedestrian request input and a third property to check
K.1
Move the terminal-count test into the controller. What breaks, and why is it worse?

## Slide 90
LAB L
From a Module to an IP
Chip Design Associate · Module 2 · Verilog RTL Coding for Synthesis · Topic 2: RTL Design Methodology
M2-T2 · 90
$ make reuse
delayline mismatches : 0 prescaler ratio errors : 0
delayline #(W=8, N) synthesised at four different depths:
N = 1 8 cells 8 flip-flops
N = 2 16 cells 16 flip-flops
N = 4 32 cells 32 flip-flops
N = 8 64 cells 64 flip-flops
Exercise
Task
L.1
Predict the cell count for N = 16 before running it
L.2
Add a bypass parameter that removes the registers entirely when N = 0
L.3
Instantiate counter_n three times to divide by 4096, and check the ratio
L.2 is the one worth arguing about
A generate loop with N = 0 builds nothing, so dout must come straight from din. Getting that right means understanding that the parameter is resolved before any hardware exists — which is the whole point of the lab.

## Slide 91
LABS M–N
Two Languages, the Whole Flow, and the Vendor Tools
Chip Design Associate · Module 2 · Verilog RTL Coding for Synthesis · Topic 2: RTL Design Methodology
M2-T2 · 91
$ make langs
=== Verilog: iverilog === === VHDL: ghdl ===
IDENTICAL over all 18 cycles - including the wrap and the terminal count.
IDENTICAL over all 17 cycles, detections included. (the '101' detector)
$ make flow
STAGE 2 LINT 0 issues
STAGE 4 SYNTHESIS 12 cells
STAGE 6 COMPARE IDENTICAL on all 18 cycles
STAGE 7 PROVE Equivalence PROVEN by induction
All seven stages passed.
Lab N: the same design in Vivado
Read the design, synthesise for a real part, report utilisation, write the netlist for gate-level simulation. Vivado is not installed in the environment these materials were built in, so lab N is the one whose output is not reproduced here — run it and record what you get.

## Slide 92
PRACTICAL · VENDOR
The Same Flow in Vivado and ModelSim
Chip Design Associate · Module 2 · Verilog RTL Coding for Synthesis · Topic 2: RTL Design Methodology
M2-T2 · 92
Stated plainly on the slide: these commands were not run here. Every number in this deck came from the free toolchain.

## Slide 93
LABS · ASSESSMENT
How the 103 Exercises Are Weighted
Chip Design Associate · Module 2 · Verilog RTL Coding for Synthesis · Topic 2: RTL Design Methodology
M2-T2 · 93
Predict, then measure. Being wrong and knowing why is the whole point of a lab.

## Slide 94
PRACTICAL · LIMITS
What This Lab Does Not Show You
Chip Design Associate · Module 2 · Verilog RTL Coding for Synthesis · Topic 2: RTL Design Methodology
M2-T2 · 94
▪
rtl_lint.py is regular expressions, not a Verilog parser. It reads code the way a careful reviewer skims it and can be fooled by unusual formatting.
▪
The cell counts come from Yosys' generic library, not a foundry library. They compare designs against each other; they are not area figures.
▪
fa_switch.v is a functional transistor model. There are no threshold voltages and no capacitances — SPICE is the tool for that.
▪
Yosys accepts initial blocks because it targets FPGAs. An ASIC flow would not, and that difference is a genuine trap.
▪
Vivado and ModelSim were not run. Every measured number here came from iverilog, ghdl and yosys, and is reproducible with make.
▪
Nothing here covers verification methodology beyond a directed testbench and a handful of assertions — that is Topic 5, a large subject on its own.
▪
The state machines here are small and single-clock. Clock-domain crossing, reset synchronisers and safe-state recovery are all real, and all later.

## Slide 95
SUMMARY
Topic 2 In Fourteen Lines
Chip Design Associate · Module 2 · Verilog RTL Coding for Synthesis · Topic 2: RTL Design Methodology
M2-T2 · 95
▪
RTL says which registers exist and what transfers into them. Nothing else.
▪
There are two kinds of logic, combinational and sequential, and no third.
▪
<= reads every right-hand side first, then updates together. = does not — and the blocking version built 1 flip-flop where 3 were meant.
▪
Four levels of abstraction describe the same circuit — proved, not assumed.
▪
Write at the highest level that says what you mean: behavioural gave 5 cells against 6.
▪
Not all legal Verilog is synthesisable, and a / b cost 371 cells against 0.
▪
A combinational block that does not assign on every path builds a latch; a default assignment at the top of the block prevents it.
▪
An incomplete sensitivity list makes simulation and silicon disagree silently.
▪
Equivalent is not identical: three mux styles, 3, 6 and 10 cells.
▪
Almost every block is a datapath and a controller. Here: 145 cells against 10.
▪
Write state machines in three blocks — register, next state, output.
▪
Moore trails Mealy by exactly one cycle, and one-hot was BIGGER here.
▪
parameter, hierarchy and generate are elaborated away before synthesis.
▪
Verilog and VHDL produced identical transcripts, on both designs.

## Slide 96
CLOSE
What To Do Next
Chip Design Associate · Module 2 · Verilog RTL Coding for Synthesis · Topic 2: RTL Design Methodology
M2-T2 · 96
Coming next in Module 2
Topic 3 covers the digital logic this all rests on. Topic 4 writes much more RTL. Topic 5 is verification — how you know it works. Topic 6 is timing — whether it is fast enough.